Live Jamming Protocol (LJP)

UDP packet description :

---------------------------------------------- ----------------------------------------------------------------------
| proto[4bit] | componentId[10bit] | requestId[6bit] |sessionId[32bit] | datalen[12] | |\\| datas[...] |
---------------------------------------------- ----------------------------------------------------------------------

Proto id :	version 1	1

Components id :	- session	1
- channel	2
- room	3
- jam	4

Connection Steps :

 Step 1: Client requests session with server:
{
 componentId :	SESSION_COMPONENTID	1

 requestId :	SESSION_AUTHREQUEST	1

 sessionId :	SESSION_ID	0

 datas :	login
password
}

packet format example:

---------------------------------------------------------------------------------------------------------------------------- -------------------------------------------------------------------
PROTO | SESSION_COMPONENTID | SESSION_AUTHREQUEST | SESSION_ID | DATALEN | DATAS = null_terminated_login,null_terminated_pass |
---------------------------------------------------------------------------------------------------------------------------- -------------------------------------------------------------------

 Step 2: Server informs client that session has been created:
{
 componentId :	SESSION_COMPONENTID	1

 requestId :	SESSION_AUTHREQUEST_OK	2

 sessionId :	SESSION_ID	X

 datas :	user informations
}

packet format example:

---------------------------------------------------------------------------------------------------------------------------- ---------------------------------------------------
PROTO | SESSION_COMPONENTID | SESSION_AUTHREQUEST_OK | SESSION_ID | DATALEN | DATAS = null_terminated_userinfos |
---------------------------------------------------------------------------------------------------------------------------- ---------------------------------------------------

 Step 2 (alt): Server informs client that session has NOT beed created, bad authentification:
{
 componentId :	SESSION_COMPONENTID	1

 requestId :	SESSION_AUTHREQUEST_NOK_BADAUTH	3

 sessionId :	SESSION_ID	0
}

packet format example:

---------------------------------------------------------------------------------------------------------------------------- -------------------------------------------
PROTO | SESSION_COMPONENTID | SESSION_AUTHREQUEST_NOK_BADAUTH | SESSION_ID | DATALEN | DATAS = nul l |
---------------------------------------------------------------------------------------------------------------------------- -------------------------------------------

 Step 2 (alt): Server informs client that session has NOT beed created, authentification duplicate:
{
 componentId :	SESSION_COMPONENTID	1

 requestId :	SESSION_AUTHREQUEST_NOK_DUPLICATE	3

 sessionId :	SESSION_ID	0
}

packet format example:

---------------------------------------------------------------------------------------------------------------------------- ---------------------------------------------
PROTO | SESSION_COMPONENTID | SESSION_AUTHREQUEST_NOK_DUPLICATE | SESSION_ID | DATALEN | DATAS = nul l |
---------------------------------------------------------------------------------------------------------------------------- ---------------------------------------------

 Step 3 : Client disconnects from server :
{
 componentId :	SESSION_COMPONENTID	1

 requestId :	SESSION_DISCONNECT	5

 sessionId :	SESSION_ID	0
}

packet format example:

---------------------------------------------------------------------------------------------------------------------------- ----------------
PROTO | SESSION_COMPONENTID | SESSION_DISCONNECT | SESSION_ID | DATALEN | DATAS = nul l |
---------------------------------------------------------------------------------------------------------------------------- ----------------

 Step 3 : Server disconnects from client:
{
 componentId :	SESSION_COMPONENTID	1

 requestId :	SESSION_DISCONNECTED	6

 sessionId :	SESSION_ID	0
}

packet format example:

---------------------------------------------------------------------------------------------------------------------------- --------------------
PROTO | SESSION_COMPONENTID | SESSION_DISCONNECTED | SESSION_ID | DATALEN | DATAS = nul l |
---------------------------------------------------------------------------------------------------------------------------- --------------------

Channel / Message Steps :

CHANNEL_ID =	16bit
CLIENT_SESSION_ID =	32bit

 User Join Channel :
{
 componentId :	CHANNEL_COMPONENTID	2

 requestId :	CHANNEL_JOIN	1

 sessionId :	SESSION_ID	X

 datas :	CHANNEL_ID	X
}

packet format example:

---------------------------------------------------------------------------------------------------------------------------- -----------------------
PROTO | CHANNEL_COMPONENTID | CHANNEL_JOIN | SESSION_ID | DATALEN | DATAS = CHANNEL_ID |
---------------------------------------------------------------------------------------------------------------------------- -----------------------

 User receive joined notification of a user in the Channel :
{
 componentId :	CHANNEL_COMPONENTID	2

 requestId :	CHANNEL_JOINED	4

 sessionId :	SESSION_ID	X

 datas :	CHANNEL_ID	X
CLIENT_SESSION_ID	X
}

packet format example:

---------------------------------------------------------------------------------------------------------------------------- ----------------------------
PROTO | CHANNEL_COMPONENTID | CHANNEL_LEAVED | SESSION_ID | DATALEN | DATAS = CHANNEL_ID |
---------------------------------------------------------------------------------------------------------------------------- ----------------------------

 User leave Channel :
{
 componentId :	CHANNEL_COMPONENTID	2

 requestId :	CHANNEL_LEAVE	10

 sessionId :	SESSION_ID	X

 datas :	CHANNEL_ID	X
}

packet format example:

---------------------------------------------------------------------------------------------------------------------------- -----------------------
PROTO | CHANNEL_COMPONENTID | CHANNEL_JOIN | SESSION_ID | DATALEN | DATAS = CHANNEL_ID |
---------------------------------------------------------------------------------------------------------------------------- -----------------------

 User receive leaved notification of a user in the Channel :
{
 componentId :	CHANNEL_COMPONENTID	2

 requestId :	CHANNEL_LEAVED	13

 sessionId :	SESSION_ID	X

 datas :	CHANNEL_ID	X
CLIENT_SESSION_ID	X
}

packet format example:

---------------------------------------------------------------------------------------------------------------------------- ----------------------------
PROTO | CHANNEL_COMPONENTID | CHANNEL_LEAVED | SESSION_ID | DATALEN | DATAS = CHANNEL_ID |
---------------------------------------------------------------------------------------------------------------------------- ----------------------------

 Send channel message :
{
 componentId :	CHANNEL_COMPONENTID	2

 requestId :	CHANNEL_MESSAGE	6

 sessionId :	SESSION_ID	X

 datas :	CHANNEL_ID	X
MESSAGE	X
}

packet format example:

---------------------------------------------------------------------------------------------------------------------------- ----------------------------------------------
PROTO | CHANNEL_COMPONENTID | CHANNEL_MESSAGE | SESSION_ID | DATALEN | DATAS = CHANNEL_ID / MESSAGE |
---------------------------------------------------------------------------------------------------------------------------- ----------------------------------------------

 Receive channel message :
{
 componentId :	CHANNEL_COMPONENTID	2

 requestId :	CHANNEL_MESSAGE_RECV	8

 sessionId :	SESSION_ID	X

 datas :	CHANNEL_ID	X
CLIENT_SESSION_ID	X
MESSAGE	X
}

packet format example:

---------------------------------------------------------------------------------------------------------------------------- ----------------------------------------------------------------------------------------
PROTO | CHANNEL_COMPONENTID | CHANNEL_MESSAGE_RECV | SESSION_ID | DATALEN | DATAS = CHANNEL_ID / CLIENT_SESSION_ID / MESSAGE |
---------------------------------------------------------------------------------------------------------------------------- ----------------------------------------------------------------------------------------

<<<<<STEPS TO IMPLEMENT NOT DECIDED YET>>>>>

 User informations Steps :

 Change status :
{
 sessionid :	sessionid

 type :	informations : status_changed

 datas :	status

 version :	proto_version
}

packet format example:

---------------------------------------------------------------------------------------------------------------------------- -------------------
sessionid | type = auth_request | datalen = ... | proto_version = ...| [datas] = null_terminated_login,null_terminated_pass |
---------------------------------------------------------------------------------------------------------------------------- -------------------

 Get user profil :
{
 sessionid :	sessionid

 type :	informations : get_profil

 datas :	user

 version :	proto_version
}

packet format example:

---------------------------------------------------------------------------------------------------------------------------- -------------------
sessionid | type = auth_request | datalen = ... | proto_version = ...| [datas] = null_terminated_login,null_terminated_pass |
---------------------------------------------------------------------------------------------------------------------------- -------------------

 Evaluate latency :
{
 sessionid :	sessionid

 type :	informations : evaluate_latency

 datas :	latency

 version :	proto_version
}

packet format example:

---------------------------------------------------------------------------------------------------------------------------- -------------------
sessionid | type = auth_request | datalen = ... | proto_version = ...| [datas] = null_terminated_login,null_terminated_pass |
---------------------------------------------------------------------------------------------------------------------------- -------------------

 Room Steps :

 Create room :
{
 sessionid :	sessionid

 type :	jam : create

 datas :	room_name
room_settings
room_participants

 version :	proto_version
}

packet format example:

---------------------------------------------------------------------------------------------------------------------------- -------------------
sessionid | type = auth_request | datalen = ... | proto_version = ...| [datas] = null_terminated_login,null_terminated_pass |
---------------------------------------------------------------------------------------------------------------------------- -------------------

 Leave room :
{
 sessionid :	sessionid

 type :	jam : end

 datas :	room_name
room_participants

 version :	proto_version
}

packet format example:

---------------------------------------------------------------------------------------------------------------------------- -------------------
sessionid | type = auth_request | datalen = ... | proto_version = ...| [datas] = null_terminated_login,null_terminated_pass |
---------------------------------------------------------------------------------------------------------------------------- -------------------

 Send invitation to room :
{
 sessionid :	sessionid

 type :	jam : invite

 datas :	room_name
room_invited
room_invitation_message

 version :	proto_version
}

packet format example:

---------------------------------------------------------------------------------------------------------------------------- -------------------
sessionid | type = auth_request | datalen = ... | proto_version = ...| [datas] = null_terminated_login,null_terminated_pass |
---------------------------------------------------------------------------------------------------------------------------- -------------------

 Receive invitation to a room :
{
 sessionid :	sessionid

 type :	jam : invite

 datas :	room_name
room_host
room_invitation_message

 version :	proto_version
}

packet format example:

---------------------------------------------------------------------------------------------------------------------------- -------------------
sessionid | type = auth_request | datalen = ... | proto_version = ...| [datas] = null_terminated_login,null_terminated_pass |
---------------------------------------------------------------------------------------------------------------------------- -------------------

 Send kick from room :
{
 sessionid :	sessionid

 type :	jam : kick

 datas :	room_name
room_kicked
room_kick_reason

 version :	proto_version
}

packet format example:

---------------------------------------------------------------------------------------------------------------------------- -------------------
sessionid | type = auth_request | datalen = ... | proto_version = ...| [datas] = null_terminated_login,null_terminated_pass |
---------------------------------------------------------------------------------------------------------------------------- -------------------

 Receive kick from a room :
{
 sessionid :	sessionid

 type :	jam : kick

 datas :	room_name
room_host
room_kick_reason

 version : proto_version
}

packet format example:

---------------------------------------------------------------------------------------------------------------------------- -------------------
sessionid | type = auth_request | datalen = ... | proto_version = ...| [datas] = null_terminated_login,null_terminated_pass |
---------------------------------------------------------------------------------------------------------------------------- -------------------

 Room settings :
{
 sessionid :	sessionid

 type :	jam : settings

 datas :	room_name
room_settings

 version :	proto_version
}

packet format example:

---------------------------------------------------------------------------------------------------------------------------- -------------------
sessionid | type = auth_request | datalen = ... | proto_version = ...| [datas] = null_terminated_login,null_terminated_pass |
---------------------------------------------------------------------------------------------------------------------------- -------------------

Jam Steps :

 Start jam :
{
 sessionid :	sessionid

 type :	jam : start

 datas :	room_name

 version :	proto_version
}

packet format example:

---------------------------------------------------------------------------------------------------------------------------- -------------------
sessionid | type = auth_request | datalen = ... | proto_version = ...| [datas] = null_terminated_login,null_terminated_pass |
---------------------------------------------------------------------------------------------------------------------------- -------------------

 Record jam :
{
 sessionid :	sessionid

 type :	jam : record

 datas :	room_name

 version :	proto_version
}

packet format example:

---------------------------------------------------------------------------------------------------------------------------- -------------------
sessionid | type = auth_request | datalen = ... | proto_version = ...| [datas] = null_terminated_login,null_terminated_pass |
---------------------------------------------------------------------------------------------------------------------------- -------------------

 Stop jam :
{
 sessionid :	sessionid

 type :	jam : stop

 datas :	room_name

 version :	proto_version
}

packet format example:

---------------------------------------------------------------------------------------------------------------------------- -------------------
sessionid | type = auth_request | datalen = ... | proto_version = ...| [datas] = null_terminated_login,null_terminated_pass |
---------------------------------------------------------------------------------------------------------------------------- -------------------